## Slide 1: Cetane Improvers – Use & Benefits
NEW DIMENSION LOGISTICS - JANUARY 2015

## Slide 2: What We Will Cover Today (While Waiting For The Sloth)
Cetane number and index
How cetane influences fuel in an engine
Why and when cetane improvers should be used
Expected benefits

## Slide 3: Cetane Number – Terms To Understand
Compression ignition is the means in which combustion in a diesel engine is achieved. Rapid compression of the air within the engine’s cylinders generates the heat required to ignite the fuel as it is injected.
Ignition quality is a measure of the ease in which combustion is initiated.
Cetane is defined as a measure of the ignition quality of a diesel fuel. It is based on the ignition delay of an engine.

## Slide 4: Cetane Number – Terms To Understand
Ignition delay is an initial phase of combustion, which follows compression, when the in-cylinder pressures and air temperatures have been considerably increased.
ASTM defines cetane number as a measure of the ignition performance of a diesel fuel that is attained by comparing it to reference fuels in a standardized engine test.
  The cetane number is indicative of how readily a fuel auto-ignites (performs)

## Slide 5: Compression Ignition Engines

## Slide 6: Compression Ignition Engines

## Slide 7: Diesel Ignition Delay

## Slide 8: Cetane Number Measurement
(CFR) Cetane Engine method, ASTM D613.
  The test utilizes a standard single cylinder, four-stroke cycle, variable compression ratio, indirectly injected diesel engine.
Cetane number of a diesel fuel is determined by varying the compression ratio (hand wheel reading) for the sample and each of two bracketing reference fuels to obtain a specific ignition delay. This permits the interpolation of cetane number in terms of hand wheel reading.
Primary reference fuels are normal cetane and heptamethylnonane. Normal cetane has been assigned a cetane number of 100. Heptamethylnonane has been assigned a cetane number of 15. The volumetrically proportioned mixtures of these fuels define the cetane number scale.
Notes: The most universally accepted cetane number measurement test is the Cooperative Fuel Research Committee (CFR) Cetane Engine method, ASTM D613. The test utilizes a standard single cylinder, four-stroke cycle, variable compression ratio, indirectly injected diesel engine.
Cetane number of a diesel fuel is determined by varying the compression ratio (hand wheel reading) for the sample and each of two bracketing reference fuels to obtain a specific ignition delay. This permits the interpolation of cetane number in terms of hand wheel reading.
The primary reference fuels are normal cetane and heptamethylnonane. Normal cetane has been assigned a cetane number of 100. Heptamethylnonane has been assigned a cetane number of 15. The volumetrically proportioned mixtures of these fuels define the cetane number scale by the following relationship:
Cetane Number = % n-cetane (vol.) + [0.15 x % heptamethylnonane (vol.)]

## Slide 9: Cetane Index
Cetane index is a calculated cetane number based on gravity (fuel density) and distillation recovery temperature.
It’s used to estimate the ASTM cetane number. It is not an optional method for expressing the ASTM cetane number.
Cetane index will not account for the presence of cetane improver -- the addition of cetane improver does not change the gravity or distillation recovery temperature of the fuel.
Cetane index is determined by either ASTM D976-91 or ASTM D4737.
This method is not accurate for Ultra Low Sulfur Diesel or Biodiesel Blends.

## Slide 10: Ways To Improve Cetane
The cetane number of diesel fuels can be increased by the use of cetane improving additives or through upgrading the fuel by hydrogenation.
Cetane improvers function to reduce the time between fuel injection and the start of combustion
The most commonly used additive compounds are
  2-ethylhexyl nitrate (2EHN)
  di-tertiarybutyl peroxide (DTBP)

## Slide 11: Higher Cetane Numbers Mean Shorter Ignition Delays

## Slide 12: Cetane Improvers from Bell Performance
Bell Performance offers several options for cetane improver.
Super Tane = aftermarket cetane improver formulation
1:1000 treat rate
Super Tane RB = concentrated cetane improver for bulk fuel treatment
1:5000 treat rate
Bell Performance also offers cetane improver blended into its diesel multifunctional formulas Dee-Zol and Dee-Zol Plus.

## Slide 13: Cetane Improver Performance
Notes: 500 ppm = 1:2000 treat rate
1000 ppm = 1:1000 treat rate

## Slide 14: Typical Cetane Improvement with Super Tane (2 Ethylhexyl nitrate or EHN)
Notes: Note that these are ranges of response. Cetane improvement is not an exact, 2+2=4 science. So you set up ranges of expectation.
Fuel response depends on starting cetane and fuel density.

## Slide 15: Why and When To Use Cetane Improvers
Cetane improvers have opportunity to add real value for customers in certain areas
To add value to premium diesel packages or multifunctionals
Differentiate product (for fuel distributors)
Help meet emissions-specific target goals
Urban users
Underground Mines
To upgrade refinery diesel to meet the desired specifications
When the refinery blending program gives a cetane deficit and a “molecule” solution is wanted
Notes: We already offer cetane improver in DZL for point #1
Helps emissions if the engines are using subpar cetane fuel
Urban users = helps with emissions

## Slide 16: Benefits To Expect From Cetane Improvers
Raising fuel cetane number through an additive can provide specific benefits to the right users:
Improved cold-weather starting
Reduced fuel consumption (up to 4%)
Reduced exhaust emissions (HC, CO, NOx and particulate emissions)
Less white smoke (unburned fuel)
Reduced warm-up time
Reduced engine noise
Improved engine durability
Notes: Explain cold weather starting
Fuel consumption – do not have specifics

## Slide 17: Effect of CN on HC Emissions

## Slide 18: Effect of CN on CO Emissions

## Slide 19: Effect of CN on NOx Emissions

## Slide 20: Effect of CN on PM

## Slide 21: Effect of CN on White Smoke in a DI Diesel Engine

## Slide 22: Noise Reduction
    Detergent package in Dee-Zol may also reduce engine noise
    Higher cetane fuels = reduced engine noise

## Slide 23: Cetane Improvers Benefit for Refiners
Fuel refiners benefit from cetane improvers:
Allows blending of low cetane stocks such as light cycle oil into diesel fuel to make a satisfactory on-spec product
More economical than hydrotreating for many refiners
Cetane trimming agent for off-specification diesel fuels
Provides cetane improvement during refinery upsets
Notes: Don’t have financial information on the difference with hydrotreating.
Not sure what they mean about refinery upsets

## Slide 24: Other Important Facts & Considerations
While cetane improvers are an important part of the fuel treatment arsenal, there are some considerations.
Fuels vary in response to CNI
2 EHN can degrade thermal stability of fuels
2 EHN can degrade lubricity levels of fuels
The ASTM minimum specification for cetane is 40. In Europe, it is 45. However, there has been talk to raising the minimum to 42.
Remember, too, that cetane improvers will not impart extra benefit to an engine that is already meeting its cetane requirement.

## Slide 25: In Review
Cetane improvers are useful to improve engine performance in multiple areas.
Super Tane (1:1000) is formulated for consumer aftermarket use
Super Tane RB (1:5000 adj) is formulated for bulk treatment at the industrial or refinery level.